## Slide 1: Implementing a SGB to GBC conversion

## Slide 2: Introduction and Assumptions
Assuming we are using a GBC for logical jumps

## Slide 3: 1. shinpokered: home.asm | Start::
Register | Value
AF | 1180
BC | 0000
DE | FF56
HL | 000D
SP | FFFE
Flag | Value
Z | 1
N | 0
H | 0
C | 0
init.asm:
SECTION "Entry", ROM0 [$100]
nop
jp Start SECTION "Header", ROM0 [$104]
; The header is generated by rgbfix.
; The space here is allocated to prevent code from being overwritten.
ds $150 - $104
SECTION "Main", ROM0
Start::
cp GBC
jr z, .gbc
xor a
jr .ok
.gbc
ld a, 1 ;gbctest - set the marker for being in gbc mode
.ok
ld [hGBC], a
jp Init
Register | Value
AF | 01C0
BC | 0000
DE | FF56
HL | 000D
SP | FFFE
Flag | Value
Z | 1
N | 1
H | 0
C | 0
Beginning
End
Code Comments:
This is the first portion of code to run after the Gameboy bootrom, starting at address $100. We nop then jump to Start (see below)
Header info left blank to be overwritten by the compiler
Compare the value in Reg A to constant GBC. Since we are in a GBC, Reg A initializes to $11, so the compare gives a zero result and the Z flag is high. N flag also high because we did a subtraction.
If the result of ‘cp GBC’ is zero, jump relative to .gbc code. If it was not, do a ‘xor a’ to set Reg A to 0 then jump relative to .ok.
Load Reg A with value 1 when executing .gbc
.ok runs regardless of whether we’re in a GBC or not.
Load the value of address hGBC with the value from Reg A (1 for GBC, 0 for not)
Jump to Init.
GBC EQU $11
hardware_constants.asm
hGBC EQU $FFFE ;gbcnote - 0 if DMG, != 0 if GBC, =2 for gamma shader
hram.asm
Summary: check Reg A to see if it is equal to $11 upon system boot. If it is set the flag that lives at hGBC in Hi RAM to 1, otherwise set hGBC to 0.

## Slide 4: 2. shinpokered: init.asm | Init::
Register | Value
AF | 01C0
BC | 0000
DE | FF56
HL | 000D
SP | FFFE
Flag | Value
Z | 1
N | 1
H | 0
C | 0
init.asm:
Init::
; Program init.
rLCDC_DEFAULT EQU %11100011
; * LCD enabled
; * Window tile map at $9C00
; * Window display enabled
; * BG and window tile data at $8800
; * BG tile map at $9800
; * 8x8 OBJ size
; * OBJ display enabled
; * BG display enabled
di
xor a
ld [rIF], a
ld [rIE], a
ld [rSCX], a
ld [rSCY], a
ld [rSB], a
ld [rSC], a
ld [rWX], a
ld [rWY], a
ld [rTMA], a
ld [rTAC], a
ld [rBGP], a
ld [rOBP0], a
ld [rOBP1], a
ld a, rLCDC_ENABLE_MASK
ld [rLCDC], a
call DisableLCD
Register | Value
AF | 8080
BC | 0000
DE | FF56
HL | 000D
SP | FFFC
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Code Comments:
This is the initialize code- it only runs once at the beginning of the program and is used to set a bunch of values.
Set constant rLCDC_DEFAULT to a binary value with each bit based on the comments there in the code.
Disable interrupts
Set Reg A to 0 via ‘xor a’, N flag goes low
Set the values that live at all of these addresses to 0
Set Reg A to the value of rLCDC_ENABLE_MASK
Load rLCDC with the resulting value
Call DisableLCD. This pushes the address after the call on to the stack so that RET can pop it later. SP is now FFFC after decrement 2
rLCDC EQU $ff40 ; LCD Control (R/W)
rLCDC_ENABLE EQU 7
rLCDC_ENABLE_MASK EQU 1 << rLCDC_ENABLE
hardware_constants.asm
Summary: Disable interrupts, zero out a bunch of hardware registers and set up for the DisableLCD call
rIF EQU $ff0f ; Interrupt Flag (R/W)
rIE EQU $ffff ; Interrupt Enable (R/W)
rSCX EQU $ff43 ; Scroll X (R/W)
rSCY EQU $ff42 ; Scroll Y (R/W)
rSB EQU $ff01 ; Serial transfer data (R/W)
rSC EQU $ff02 ; Serial Transfer Control (R/W)
rWX EQU $ff4b ; Window X Position minus 7 (R/W)
rWY EQU $ff4a ; Window Y Position (R/W)
rTMA EQU $ff06 ; Timer Modulo (R/W)
rTAC EQU $ff07 ; Timer Control (R/W)
rBGP EQU $ff47 ; BG Palette Data (R/W) - Non CGB Mode Only
rOBP0 EQU $ff48 ; Object Palette 0 Data (R/W) - Non CGB Mode Only
rOBP1 EQU $ff49 ; Object Palette 1 Data (R/W) - Non CGB Mode Only
hardware_constants.asm (lines vary)

## Slide 5: 3. shinpokered: home.asm | DisableLCD::
Register | Value
AF | 8080
BC | 0000
DE | FF56
HL | 000D
SP | FFFC
Flag | Value
Z | 1
N | 0
H | 0
C | 0
home.asm:
DisableLCD::
xor a
ld [rIF], a
ld a, [rIE]
ld b, a
res 0, a
ld [rIE], a
.wait
ld a, [rLY]
cp LY_VBLANK
jr nz, .wait
ld a, [rLCDC]
and $ff ^ rLCDC_ENABLE_MASK
ld [rLCDC], a
ld a, b
ld [rIE], a
ret
Register | Value
AF | 00A0
BC | 0000
DE | FF56
HL | 000D
SP | FFFE
Flag | Value
Z | 1
N | 0
H | 1
C | 0
Beginning
End
Code Comments:
Set Reg A to 0 via ‘xor a’ (AF to 0080)
Set rIF to 0
Load the rIE value (interrupt enable) in to Reg A. As you may recall from Init::, this value was zerod out, so A is zero
Load rIE value from A to B. Zeros for both.
Set bit 0 in Reg A to 0. Bit 0 is the rightmost one
Load the new Reg A value to rIE. In effect, set the interrupt enable to 0
Load Reg A with the value from rLY
Compare A with LY_VBLANK
If the value is not zero, then loop until it is. This code is effectively waiting for the active LCD control line to be equal to the Vblank line (145). N flag goes high when we hit not zero.
Load Reg A with the value from LCD control
AND Reg A with $FF XOR $80 (that value is $7F)
Load the resulting value in to rLCDC (value goes to $80). AND instructions cause H flag high, N low.
Load the value from B to A (this is still 0 from earlier)
Load rIE with 0 via Reg A.
Return from where we were called, putting the stack back where it was (increment 2)
Summary: Adjust interrupts a bunch, wait for the LCD controller to get to the Vblank line and return.
rIF EQU $ff0f ; Interrupt Flag (R/W)
rIE EQU $ffff ; Interrupt Enable (R/W)
rLCDC EQU $ff40 ; LCD Control (R/W)
rLCDC_ENABLE EQU 7
rLCDC_ENABLE_MASK EQU 1 << rLCDC_ENABLE
rLY EQU $ff44 ; LCDC Y-Coordinate (R)
LY_VBLANK EQU 145
hardware_constants.asm (lines vary)
Note that rLCDC_ENABLE_MASK is 1 << 7, which is $80

## Slide 6: 4. shinpokered: init.asm | after call DisableLCD
Register | Value
AF | 00A0
BC | 0000
DE | FF56
HL | 000D
SP | FFFE
Flag | Value
Z | 1
N | 0
H | 1
C | 0
init.asm:
call DisableLCD
… ld sp, wStack
ld hl, $c000 ; start of WRAM
ld bc, $2000 ; size of WRAM
.loop
ld [hl], 0
inc hl
dec bc
ld a, b
or c
jr nz, .loop
;do a bunch of RNG stuff, kinda ignoring this.
ld hl, wRNGState
ld a, [$ffb1]
ld [hli], a
ld a, [$ffd5]
ld [hli], a
ld a, $be
ld [hli], a
ld [hl], $ef
call ClearVram
Register | Value
AF | BE80
BC | 0000
DE | FF56
HL | CF29
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Code Comments:
This is where we pick up
Load the stack pointer with the address of wStack (working RAM stack)- DFFF
Load HL to value $C000
Load BC to value $2000
In a loop, set the value at HL (starting at $C000) to 0. Increment HL and decrement BC.
Load the value from B to A. OR A with C.
As long as the result is not zero, loop.
What this does in effect is clear out work RAM starting at $C000 and going for $2000 entries.
HL keeps going up and up while BC keeps going down. Since the only time when B OR C is going to equal not-zero is when B AND C are both zero we execute for the total number of times that BC initializes with ($2000)
There’s a bunch of RNG setup stuff, glossing over. Then we call ClearVram.
Summary: Clear out work RAM. Set up RNG. Call ClearVram
SECTION "Stack", WRAM0[$df00]
ds $ff
wStack:: ; dfff
wram.asm

## Slide 7: 5. shinpokered: init.asm | ClearVram, home.asm | FillMemory
Register | Value
AF | 00A0
BC | 0000
DE | FF56
HL | 000D
SP | FFFE
Flag | Value
Z | 1
N | 0
H | 1
C | 0
init.asm:
ClearVram:
ld hl, $8000
ld bc, $2000
xor a
jp FillMemory
home.asm:
FillMemory::
; Fill bc bytes at hl with a.
push de
ld d, a
.loop
ld a, d
ld [hli], a
dec bc
ld a, b
or c
jr nz, .loop
pop de
ret
Register | Value
AF | 0080
BC | 0000
DE | FF56
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Code Comments:
Load HL with value $8000
Load BC with value $2000
XOR A to get A to 0
Jump to FillMemory, decrement SP
Push DE to the top of the stack
Load D with value from A ($0)
In a loop, load A with value from D ($0)
Load data at HL with value from A ($0) and increment HL
Decrement BC until B OR C is 0, similar to what we saw previously, basically clearing out VRAM starting at address $8000 and going for $2000 addresses
Pop DE back on to the stack and return form where we were called.
Summary: Clear VRAM registers starting at $8000 going to $A000 then return.

## Slide 8: 6. shinpokered: init.asm, home.asm | FillMemory, ClearSprites
Register | Value
AF | 0080
BC | 0000
DE | FF56
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
call ClearVram
… ld hl, $ff80
ld bc, $fffe - $ff80 ;gbcnote - don't clear hGBC
call FillMemory
call ClearSprites
ClearSprites::
xor a
ld hl, wOAMBuffer
ld b, 40 * 4
.loop
ld [hli], a
dec b
jr nz, .loop
ret
Register | Value
AF | 00C0
BC | 0000
DE | FF56
HL | C3A0
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
Beginning
End
Code Comments:
Pick up where we left off in init.asm
Set HL to $FF80
Set BC to the result of $FFFE - $FF80. Because hGBC is at $FFFE we don’t want to clear it.
We saw FillMemory previously, so now we take the value in A ($0) and put it in HL up until the BC value. These values are all HI RAM, so basically we keep clearing out the system to ensure there’s no garbage data
When we’re done doing the FillMemory clearing AF is $0080, HL is $FFFE (the address for hGBC, it gets incremented to, but never touched)
Call ClearSprites, SP decrements
Set A to 0 via ‘xor a’
Set HL to the address for wOAMBuffer, $C300
Set B to the value 40 * 4 ($A0). This is consistent with the defined size from wram.asm
In a loop zero out the data at address HL and increment, decrement B and compare to A.
In effect, a similar loop as what we saw previously, now just clearing data starting at $C300 going to $C3A0.
Summary: Clear Hi RAM, Clear Sprite data at $C300.
SECTION "OAM Buffer", WRAM0[$c300]
wOAMBuffer:: ; c300
; buffer for OAM data. Copied to OAM by DMA
ds 4 * 40
wram.asm
hGBC EQU $FFFE ;gbcnote - 0 if DMG, != 0 if GBC, =2 for gamma shader
hram.asm

## Slide 9: 7. shinpokered: init.asm, continued
Register | Value
AF | 00C0
BC | 0000
DE | FF56
HL | C3A0
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
call ClearSprites
…
ld a, Bank(WriteDMACodeToHRAM)
ld [H_LOADEDROMBANK], a
ld [MBC1RomBank], a
call WriteDMACodeToHRAM
Register | Value
AF | 01C0
BC | 0000
DE | FF56
HL | C3A0
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
Beginning
End
Code Comments:
Pick up where we left off in init.asm
Load Reg A with the Bank number for where WriteDMACodeToHRAM lives. Per the main.asm (which is the primary code that gets compiled), that particular function lives in bank $1
Load a few other variables with that bank number (H_LOADEDROMBANK and MBC1RomBank)
Then call Write DMACodeToHRAM which needs those variables to be set to the correct bank in order to proceed.
Summary: Set a couple variables to the bank number for a particular command then call WriteDMACodetoHRAM
H_LOADEDROMBANK EQU $FFB8
hram.asm
SECTION "bank1",ROMX,BANK[$1]
…
INCLUDE "engine/oam_dma.asm”
main.asm
MBC1RomBank EQU $2000
hardware_constants.asm

## Slide 10: 7. shinpokered: oam_dma.asm
Register | Value
AF | 01C0
BC | 0000
DE | FF56
HL | C3A0
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
WriteDMACodeToHRAM:
; Since no other memory is available during OAM DMA,
; DMARoutine is copied to HRAM and executed there.
ld c, $ff80 % $100
ld b, DMARoutineEnd - DMARoutine
ld hl, DMARoutine
.copy
ld a, [hli]
ld [$ff00+c], a
inc c
dec b
jr nz, .copy
ret
DMARoutine:
; initiate DMA
ld a, wOAMBuffer / $100
ld [rDMA], a
; wait for DMA to finish
ld a, $28
.wait
dec a
jr nz, .wait
ret
DMARoutineEnd:
Register | Value
AF | C9C0
BC | 008A
DE | FF56
HL | 4A6C
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
Beginning
End
Code Comments:
This whole chunk of code is made to copy DMARoutine to HI RAM. See comment here.
Load C with $FF80 modulo $100, which is $80
Load B with the difference between the addresses for DMARoutineEnd and DMARoutine (see lower down where these are defined).
Load HL with the address for DMARoutine
In a loop, copy the data located at HL’s address (ie the DMARoutine address) in to A, then use A to load that data to memory locations starting at $FF00 (beginning of HI RAM) and increasing until all the data is copied.
While we’re here, let’s look at DMARoutine
Load Reg A with the address for wOAMBuffer divided by $100.
This is $C300 / $100, which is $0
Load rDMA with the value from A ($0)
Load A with the value $28
In a loop, decrement A until it is zero. Effectively 28 ticks of the CPU
Summary: Copy the DMARoutine code to HiRAM. DMARoutine does a DMA data transfer for $28 clock ticks.
H_LOADEDROMBANK EQU $FFB8
hram.asm
SECTION "bank1",ROMX,BANK[$1]
…
INCLUDE "engine/oam_dma.asm”
main.asm
rDMA EQU $ff46 ; DMA Transfer and Start Address (W)
hardware_constants.asm
SECTION "OAM Buffer", WRAM0[$c300]
wOAMBuffer:: ; c300
; buffer for OAM data. Copied to OAM by DMA
ds 4 * 40
wram.asm

## Slide 11: 8. shinpokered: init.asm continued
Register | Value
AF | C9C0
BC | 008A
DE | FF56
HL | 4A6C
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
init.asm:
call WriteDMACodeToHRAM
… xor a
ld [hTilesetType], a
ld [rSTAT], a
ld [hSCX], a
ld [hSCY], a
ld [rIF], a
ld a, 1 << VBLANK + 1 << TIMER + 1 << SERIAL
ld [rIE], a
ld a, 144 ; move the window off-screen
ld [hWY], a
ld [rWY], a
ld a, 7
ld [rWX], a
ld a, CONNECTION_NOT_ESTABLISHED
ld [hSerialConnectionStatus], a
Register | Value
AF | FF80
BC | 008A
DE | FF56
HL | 4A6C
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Summary: Set a bunch of screen-related variables to zero or set the screen values to be off-screen, then set serial connection to not established.
hTilesetType EQU $FFD7
; these values are copied to SCX, SCY, and WY during V-blank
hSCX EQU $FFAE
hSCY EQU $FFAF
hWY EQU $FFB0
; $01 = using external clock
; $02 = using internal clock
; $ff = establishing connection
hSerialConnectionStatus EQU $FFAA
hram.asm
; interrupt flags
VBLANK EQU 0
TIMER EQU 2
SERIAL EQU 3
rSTAT EQU $ff41 ; LCDC Status (R/W)
rIF EQU $ff0f ; Interrupt Flag (R/W)
rIE EQU $ffff ; Interrupt Enable (R/W)
rWY EQU $ff4a ; Window Y Position (R/W)
rWX EQU $ff4b ; Window X Position minus 7 (R/W)
hardware_constants.asm
CONNECTION_NOT_ESTABLISHED EQU $ff
misc_constants.asm
Code Comments:
Pick up in init.asm where we left off.
XOR A to set it to zero
Set a bunch of values to zero
Set A to the value of (1 << 0) + (1<<2) +(1<<3), then put that value in the interrupt enable variable. This should be $0D
Then set A to 144 and use this to set the screen to Y=144, X = 7
Set hSerialConnectionStatus to $FF, not established.

## Slide 12: 9. shinpokered: init.asm, vcopy.asm
Register | Value
AF | FF80
BC | 008A
DE | FF56
HL | 4A6C
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
init.asm:
ld [hSerialConnectionStatus], a
… ld h, vBGMap0 / $100
call ClearBgMap
ld h, vBGMap1 / $100
call ClearBgMap
vcopy.asm
; clears a VRAM background map with blank space tiles
; INPUT: h - high byte of background tile map address in VRAM
ClearBgMap::
ld a, " "
jr .next
ld a, l
.next
ld de, $400 ; size of VRAM background map
ld l, e
.loop
ld [hli], a
dec e
jr nz, .loop
dec d
jr nz, .loop
ret
Register | Value
AF | 7FC0
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
Beginning
End
Summary: Set VRAM for the two Background maps (located at $9800 and $9C00) to “ “ ($7F) using a for loop. ClearBgMap depends on the value of h when it starts and has a hard coded for iteration count of $400.
vBGMap0 EQU $9800
vBGMap1 EQU $9c00
vram.asm
charmap " ", $7F
charmap.asm
n/a
Code Comments:
Pick up in init.asm where we left off.
Load H with vBGMap0 / $100, which is $9800 / $100 = $98. Do this again for vBGMap1 after ClearBgMap. This is done to get just the 1st byte
As the notes suggest, this function clears the VRAM background map and takes whatever is in the H register as the input such that it represents the high byte of the BG tilemap address in vRAM.
Put a blank string “ “ in reg A. This is $7F per the character map.
Jump relative to .next
Not sure if this line will ever be called
Load DE with constant $400- representing the size of the VRAM BG Map
Put the value from E (lower byte, $00 if DE is $0400) in to L. At this point HL is $9800
Load the RAM at HL with the value from A ($7F, char “ “) and increment HL (goes from $9800 to $9801)
Decrement E- since it was $00, it underflows around to $FF. Keep doing this until we get a N & Z flag result, which is when ‘dec e’ results in E == 0.
We do similar with the D register, but only when we loop through all E values- this is effectively another way to do a for loop

## Slide 13: 10. shinpokered: init.asm
Register | Value
AF | 7FC0
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 1
H | 0
C | 0
init.asm
call ClearBgMap
…
ld a, rLCDC_DEFAULT
ld [rLCDC], a
ld a, 16
ld [hSoftReset], a
call StopAllSounds
init.asm (later):
StopAllSounds::
ld a, BANK(Audio1_UpdateMusic)
ld [wAudioROMBank], a
ld [wAudioSavedROMBank], a
xor a
ld [wAudioFadeOutControl], a
ld [wNewSoundID], a
ld [wLastMusicSoundID], a
jp StopAllMusic
audio.asm:
StopAllMusic::
ld a, $FF
ld [wNewSoundID], a
; plays music specified by a. If value is $ff, music is stopped
Register | Value
AF | 0180
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Summary: Set the LCD Controller to the default value then initialize hSoftReset to its default (16) and lastly stop all sound and music.
rLCDC EQU $ff40 ; LCD Control (R/W)
hardware_constants.asm
rLCDC_DEFAULT EQU %11100011
; * LCD enabled
; * Window tile map at $9C00
; * Window display enabled
; * BG and window tile data at $8800
; * BG tile map at $9800
; * 8x8 OBJ size
; * OBJ display enabled
; * BG display enabled
init.asm (much earlier)
hSoftReset EQU $FF8A
; Initialized to 16.
; Decremented each input iteration if the player
; presses the reset sequence (A+B+SEL+START).
; Soft reset when 0 is reached.
hram.asm
Code Comments:
Pick up in init.asm where we left off.
Put the value we defined much earlier for the rLCDC_DEFAULT in to A then write that value to address rLCDC.
Set hSoftReset to 16 (see hram.asm note). Basically ensures there’s a 16 CPU cycle delay before actually soft resetting.
Call StopAllSounds
Load up the Bank number where Audio1_UpdateMusic lives (this is in engine_1.asm, which is in audio.asm, which is in home.asm, which is in bank 0. Put this value in to the work ram audio ROM bank variables
Set A to 0 via ‘xor a’
set a bunch of work ram variables to 0
Call StopAllMusic
StopAllMusic basically sets work ram’s wNewSoundID with the value $FF- as the note shows this stops all music.
There’s no RET here, so it actually does the next part of the code which is PlaySound, but since this one is already long we’ll ignore that.
END register values here are representative of what it is in init.asm after StopAllSounds is done.
wAudioROMBank:: ; c0ef
ds 1 wAudioSavedROMBank:: ; c0f0
ds 1
wAudioFadeOutControl:: ; cfc7
ds 1
wNewSoundID:: ; c0ee
ds 1
wLastMusicSoundID:: ; cfca
ds 1
wram.asm

## Slide 14: Recap
Up to this point the code has zeroed out a bunch of RAM including work, video and high and vRAM background maps.
The hGBC variable has a $1 in it (and wasn’t cleared out)
Other variables have been given their default startup values.

## Slide 15: 11. shinpokered: init.asm
Register | Value
AF | 0180
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
init.asm
call StopAllSounds
…
ei
predef LoadSGB
Register | Value
AF | 0180
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Summary: Enable interrupts and do a bunch of macro business to run the code for LoadSGB
PredefPointers::
; these are pointers to ASM routines.
; they appear to be used in overworld map scripts.
…
add_predef LoadSGB
predefs.asm
n/a
n/a
Code Comments:
Pick up in init.asm where we left off.
Enable interrupts
do a predef to LoadSGB. predef is an asm macro that basically handles all the bank switching involved to get to the right ROM bank for the function in question then it goes there.
The pointers for all predefs are defined in predefs.asm
The actual code for LoadSGB lives in palettes.asm, which will get it’s own slide.

## Slide 16: 11. shinpokered: palettes.asm
Register | Value
AF | 0180
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
palettes.asm:
LoadSGB: ;gbcnote - adjust for GBC
xor a
ld [wOnSGB], a
call CheckSGB
jr c, .onSGB
ld a, [hGBC]
and a
jr z, .onDMG
;if on gbc, set SGB flag but skip all the SGB vram stuff
ld a, $1
ld [wOnSGB], a
.onDMG
ret
.onSGB
ld a, $1
ld [wOnSGB], a
di
call PrepareSuperNintendoVRAMTransfer
…
(we will skip this since it’s not relevant to GBC)
Register | Value
AF | 0180
BC | 008A
DE | 0000
HL | 66E0
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
Beginning
End
Summary: Set wOnSGB to $1 if we are on GBC but don’t run all of the SGB specific stuff.
wOnSGB:: ; cf1b
; if running on SGB, it's 1, else it's 0
ds 1
wram.asm
hGBC EQU $FFFE ;gbcnote - 0 if DMG, != 0 if GBC, =2 for gamma shader
hram.asm
n/a
Code Comments:
Clear A to 0 with ‘xor a’
Not going to detail this one, but it does a bunch of hardware checks. The end result is that if we are on SGB then a ‘scf’ set carry flag is set true.
Since we aren’t on SGB the carry flag is still 0, so we don’t jump to .onSGB. rather load the value from the hGBC variable (should be $1 from way back on the first slide).
AND A will result in a 1, not a zero, so we will not meet the criteria for .onDMG, so continue executing.
This part was added (see the note). basically put a $1 in the wOnSGB variable even though we aren’t technically on a SGB.
At this point we hit the return that lives under .onDMG and return from whence we came.
In future code blocks where wOnSGB is called we’ll need to make sure we handle them gracefully by adding additional GBC check logic so that we don’t start doing SGB VRAM stuff.

## Slide 17: 12. shinpokered: init.asm
Register | Value
AF | 0180
BC | 008A
DE | 0000
HL | A000
SP | DFFF
Flag | Value
Z | 1
N | 0
H | 0
C | 0
init.asm:
predef LoadSGB
…
ld a, BANK(SFX_Shooting_Star)
ld [wAudioROMBank], a
ld [wAudioSavedROMBank], a
ld a, $9c
ld [H_AUTOBGTRANSFERDEST + 1], a
xor a
ld [H_AUTOBGTRANSFERDEST], a
dec a
ld [wUpdateSpritesEnabled], a
predef PlayIntro
Register | Value
AF | FF80
BC | 008A
DE | 0000
HL | 66E0
SP | DFFF
Flag | Value
Z | 0
N | 1
H | 1
C | 0
Beginning
End
Summary: Get the banks set up for the intro and set the value of H_AUTOBGTRANSFERDEST (the transfer destination of the automatic background transfer code we saw earlier) to $009C
wAudioROMBank:: ; c0ef
ds 1
wAudioSavedROMBank:: ; c0f0
ds 1
wUpdateSpritesEnabled:: ; cfcb
; $00 = causes sprites to be hidden and the value to change to $ff
; $01 = enabled
; $ff = disabled
; other values aren't used
ds 1
wram.asm
; the destination address of the automatic background transfer
H_AUTOBGTRANSFERDEST EQU $FFBC ; 2 bytes
hram.asm
n/a
Code Comments:
Pick up where we left off
Now that everything has been zeroed out / initialized, we start setting up to run the intro.
Start by setting the audio banks to be the same as the SFX_Shooting_Star code
Since H_AUTOBGTRANSERDEST is 2 Bytes we set both bytes here. in effect we get $009C
dec A causes underflow, wraps to $FF, puts that value in wUpdateSpritesEnabled.
Finally predef call to PlayIntro

## Slide 18: 13. shinpokered: intro.asm
Register | Value
AF | 1000
BC | 008A
DE | 3D79
HL | 5696
SP | DFF9
Flag | Value
Z | 0
N | 0
H | 0
C | 0
intro.asm:
PlayIntro:
xor a
ld [hJoyHeld], a
inc a
ld [H_AUTOBGTRANSFERENABLED], a
call PlayShootingStar
(slide #14)
call PlayIntroScene
call GBFadeOutToWhite
xor a
ld [hSCX], a
ld [H_AUTOBGTRANSFERENABLED], a
call ClearSprites
call DelayFrame
ret
Register | Value
AF | 1000
BC | 008A
DE | 3D79
HL | 5696
SP | DFF9
Flag | Value
Z | 0
N | 0
H | 0
C | 0
Beginning
End
Summary: Not much here before PlayShootingStar except setting the hi ran auto background transfer enabled to $1.
;FFB4
hJoyHeld:: db
hram_pokered_addresses.txt
; the destination address of the automatic background transfer
H_AUTOBGTRANSFERDEST EQU $FFBC ; 2 bytes
hram.asm
n/a
Code Comments:
This code starts executing after the predef macro does its thing- beginning values here may be different than what the last end point was.
Zero out A
Set the value of hJoyHeld to 0
Increment A to $01
Set H_AUTOBGTRANSFERENABLED to $01
Call PlayShootingStar
Full dig in on PlayShootingStar on next slide
Note that I’m going to ignore a lot on there including all the gamma stuff since I’m mostly interested in just the SGB to GBC colorizing.

## Slide 19: 14. shinpokered: intro.asm, home.asm
Register | Value
AF | 1000
BC | 008A
DE | 3D79
HL | 5696
SP | DFF9
Flag | Value
Z | 0
N | 0
H | 0
C | 0
intro.asm:
PlayShootingStar:
ld b, SET_PAL_GAME_FREAK_INTRO
call RunPaletteCommand
… (PlayShootingStar continues)
home.asm:
RunPaletteCommand::
ld a, [wOnSGB]
and a
ret z
predef_jump _RunPaletteCommand
palettes.asm:
_RunPaletteCommand:
call GetPredefRegisters
ld a, b ;b holds the address of the pal command to run
cp $ff
jr nz, .next
ld a, [wDefaultPaletteCommand] ; use default command if command ID is $ff
.next
cp UPDATE_PARTY_MENU_BLK_PACKET
jp z, UpdatePartyMenuBlkPacket
ld l, a
ld h, 0
add hl, hl
ld de, SetPalFunctions
add hl, de
ld a, [hli]
ld h, [hl]
ld l, a
ld de, SendSGBPackets
push de ;by pushing de, the next 'ret' command encountered will jump to SendSGBPackets
jp hl
Register | Value
AF | 5A00
BC | 0C8A
DE | 6011
HL | 5D5A
SP | DFEF
Flag | Value
Z | 0
N | 0
H | 0
C | 0
Beginning
End
Summary: In effect, the value in Reg B is the selector for case logic that will select the proper SetPal function. In this case $0C gets us queued up to run SetPal_GameFreakIntro
SET_PAL_GAME_FREAK_INTRO EQU $0C
UPDATE_PARTY_MENU_BLK_PACKET EQU $FC
palette_constants.asm
wOnSGB:: ; cf1b
; if running on SGB, it's 1, else it's 0
ds 1
wPredefRegisters:: ; cc4f
ds 6
wDefaultPaletteCommand:: ; cf1c
ds 1
wram.asm
GetPredefRegisters::
; Restore the contents of register pairs
; when GetPredefPointer was called.
ld a, [wPredefRegisters + 0]
ld h, a
ld a, [wPredefRegisters + 1]
ld l, a
ld a, [wPredefRegisters + 2]
ld d, a
ld a, [wPredefRegisters + 3]
ld e, a
ld a, [wPredefRegisters + 4]
ld b, a
ld a, [wPredefRegisters + 5]
ld c, a
ret
predef.asm
Code Comments:
Set Reg B to the value $0C (SET_PAL_GAME_FREAK_INTRO) and call RunPaletteCommand
This one is basically a wrapper that does the wSGB check- since wOnSGB is $1 for us we will do the jump to _RunPaletteCommand
Load up the register pairs (HL, DE, BC) with the 6 byte values that live at CC4F. During the predef macro stuff these values were set to store the values of what the registers were before the predef macro was called. This restores B to $0C. This is then loaded to A
Compare A ($0C) to $FF
If the subtract compare is a not zero, jump to next, otherwise load up the value of wDefaultPaletteCommand to A. At this point that value would be 0, but we actually do jump relative to .next, so no problem there.
Compare $FC (see palette_constants.asm) to $0C. If it matches then do UpdatePartyMenuBlkPacket (we won’t here)
Load L with $0C and H with $00
Double HL by adding it to itself. Because SetPalFunctions uses dw to declare words (2 bytes each) we need to account for that.
Set DE to the address for SetPalFunctions
Add the base address for SetPalFunctions to the offset for our PalFunction ($0C, ie- SetPal_GameFreakIntro)
Set up HL to be the address for the SetPal_GameFreakIntro code and set DE to be the address for SendSGBPackets. Pushing DE then enqueues it to run after the next return we encounger.
Jump to HL, the address for the SetPal_GameFreakIntro code
SetPalFunctions: …
dw SetPal_BattleBlack …
dw SetPal_GameFreakIntro
palettes.asm

## Slide 20: 15. shinpokered: palettes.asm
Register | Value
AF | 5A00
BC | 0C8A
DE | 6011
HL | 5D5A
SP | DFEF
Flag | Value
Z | 0
N | 0
H | 0
C | 0
palettes.asm:
SetPal_GameFreakIntro:
ld hl, PalPacket_GameFreakIntro
ld de, BlkPacket_GameFreakIntro
ld a, SET_PAL_GENERIC
ld [wDefaultPaletteCommand], a
ret
Register | Value
AF | 0800
BC | 0C8A
DE | 6595 (loc.)
HL | 6690 (color)
SP | DFEF
Flag | Value
Z | 0
N | 0
H | 0
C | 0
Beginning
End
Summary: HL now contains the color information and DE contains the location information for the colors. We are getting close to finally displaying these on a GBC! Next we go to SendSGBPackets (which is where I believe we will branch off and do the GBC-specific actions needed).
PalPacket_GameFreakIntro: PAL_SET PAL_GAMEFREAK, PAL_REDMON, PAL_VIRIDIAN, PAL_BLUEMON
…
BlkPacket_GameFreakIntro:
ATTR_BLK 3
ATTR_BLK_DATA %111, 1,1,0, 05,11, 07,13 ; falling stars (left): pal 1, GameFreak logo: pal 0
ATTR_BLK_DATA %010, 2,2,0, 08,11, 09,13 ; falling stars (middle): pal 2
ATTR_BLK_DATA %011, 3,3,0, 12,11, 14,13 ; falling stars (right): pal 3
ds 12
db $03,$00,$00,$13,$0a,$00
db $03,$00,$0b,$04,$0d,$00
db $03,$05,$0b,$07,$0d,$01
db $03,$08,$0b,$13,$0d,$00
db $03,$00,$0e,$13,$11,$00
db $03,$08,$0b,$09,$0d,$02
db $03,$0c,$0b,$0e,$0d,$03
db $00
…
PAL_SET: MACRO
db ($a << 3) + 1
dw \1, \2, \3, \4
ds 7
ENDM
sgb_packets.asm
SET_PAL_GENERIC EQU $08
const_value = 0 (note these aren’t in code order which is how the program knows the value of each)
const PAL_GAMEFREAK ; $24
const PAL_REDMON ; $12
const PAL_VIRIDIAN ; $02
const PAL_BLUEMON ; $11
palette_constants.asm
Code Comments:
Here we set the palette data in the HL and DE registers.
HL will have PalPacket_GameFreakIntro which contains the actual color information.
The PAL_SET macro effectively bitpacks everything in to a single word (2 byte) packet that points to color information in memory- I believe located via super_palettes.asm
DE will have BlkPacket_GameFreakIntro which will have the ATTR_BLK information. ATTR_BLK defines the rectangular regions which each palette applies. As shown on the left, this can be quite detailed with multiple active color areas occuring at the same time.
See https://github.com/ahrnbom/gbapfomgd/blob/master/gbasmdev.tex (roughly line 1257) for more details on ATTR_BLK.
We are sending 3 blocks of ATTR_BLK data. All that said, I don’t need to mess with any of this, just to use the info loaded here on the GBC.
Load up A / wDefaultPaletteCommand with the value $08 then return. As noted in the previous slide the command SendSGBPackets has been enqueued on the stack, so this is where we go to next.

## Slide 21: 16. shinpokered: palettes.asm
Register | Value
AF | 0800
BC | 0C8A
DE | 6595 (blk)
HL | 6690 (color)
SP | DFEF
Flag | Value
Z | 0
N | 0
H | 0
C | 0
palettes.asm:
SendSGBPackets:
ld a, [hGBC];gbcnote –replaced wGBC
and a
jr z, .notGBC
push de
call InitGBCPalettes
(Next Slide)
… (SendSGBPakcets code will continue on another slide)
Register | Value
AF | 0800
BC | 0C8A
DE | 6595 (blk)
HL | 6690 (color)
SP | DFEF
Flag | Value
Z | 0
N | 0
H | 1
C | 0
Beginning
End
Summary: Check if we are on a GBC and if we are call InitGBCPalettes, which is detailed on the next slide.
hGBC EQU $FFFE ;gbcnote - 0 if DMG, != 0 if GBC, =2 for gamma shader
hram.asm
n/a
n/a
Code Comments:
Load up A with the hGBC flag and compare it. If the result is 0 go to .notGBC. Since it should result in a $1 we keep going.
Push DE (the location information) to the stack and call InitGBCPalettes.
See the next slide for details on InitGBCPalettes

## Slide 22: 17. shinpokered: palettes.asm
Register | Value
AF | 0800
BC | 0C8A
DE | 6595 (blk)
HL | 6690 (color)
SP | DFEF
Flag | Value
Z | 0
N | 0
H | 0
C | 0
palettes.asm:
InitGBCPalettes:;gbcnote - updating this to work with the Yellow code
ld a, [hl]
and $f8
cp $20 ;check to see if hl points to a blk pal packet
jp z, TranslatePalPacketToBGMapAttributes ;jump if so
;otherwise hl points to a different pal packet or wPalPacket
inc hl
index = 0
REPT NUM_ACTIVE_PALS
IF index > 0
pop hl
ENDC
ld a, [hli] ;get palette ID into 'A'
inc hl
IF index < (NUM_ACTIVE_PALS + -1)
push hl
ENDC
call GetGBCBasePalAddress ;get palette address into de
(code continues at a later slide)
Register | Value
AF | 2440
BC | 0C8A
DE | 6595 (blk)
HL | 6693
SP | DFEB
Flag | Value
Z | 0
N | 1
H | 0
C | 0
Beginning
End
Summary: For this portion, check if the HL register contains BGMapAttributes (blk data) otherwise start a loop. At this point in the loop we are going to call GetGBCBasePalAddress
NUM_ACTIVE_PALS EQU 4
misc_constants.asm
n/a
n/a
Code Comments:
This was clearly the backporting that was done.
Load A with the value that lives at HL (the color address)- in this case the value at $6690 is $51.
AND this value ($51) with $F8- result is $50
Compare $50 to $20 (which should tell us if this packet is the ATTR_BLK packet. In our case since we aren’t that packet (HL is currently color) then we keep going rather than jumping. Will need to jump through TranslatePalPacketToBGMapAttributes later.
Increment HL, now pointing at $6691
Set an index to 0
Repeat for the NUM_ACTIVE_PALS, or 4 times.
For all but the first iteration pop HL from the stack, otherwise keep going.
Load A with value from HL (address $6691, value $24) and increment HL (now $6692)
If index is less than 3, push HL to the Stack (that is the case on the first go-round here).
We now call GetGBCBasePalAddress

## Slide 23: 18. shinpokered: palettes.asm
Register | Value
AF | 2440
BC | 0C8A
DE | 6595 (blk)
HL | 6693
SP | DFEB
Flag | Value
Z | 0
N | 1
H | 0
C | 0
palettes.asm:
GetGBCBasePalAddress:: ;gbcnote - new function
; Input: a = palette ID
; Output: de = palette address
push hl
ld l, a
xor a
ld h, a
add hl, hl
add hl, hl
add hl, hl
ld de, GBCBasePalettes
add hl, de
ld a, l
ld e, a
ld a, h
ld d, a
pop hl
ret
Register | Value
AF | 
BC | 
DE | 
HL | 
SP | 
Flag | Value
Z | 
N | 
H | 
C | 
Beginning
End
Summary:
hGBC EQU $FFFE ;gbcnote - 0 if DMG, != 0 if GBC, =2 for gamma shader
hram.asm
n/a
n/a
Code Comments: